## Slide 1
Geometries for Detector Construction in Geant4
Raman Sehgal (BARC)

## Slide 2
Things to be discussed
1) Steps involved to create the detector geometries
2) Some of the complex geometries available in Geant4
3) Discussion of “Materials” in brief.
4) Geometry hierarchy in a detector setup.
5) How to import / export the geometry
6) Use of GDML
5) How to read CAD geometries.

## Slide 3
Quick Brush up of C++
1) Class is basically a user-defined data type
2) The variables of class is known as objects
3) Class contains following
(a) Data members : The variable that are defined inside the class
(b) Member functions : The functions that are defined inside the class
These member function can operate only on the variable defined inside the class
4) Constructor : A special function without any return type and is called automatically
upon creation of objects of class
5) Construct can be default (without any parameters), or parameterized constructor.
6) Its always a good practice to define constructor. These are used to set the data member
upon creation of object.

## Slide 4
10) Two types of classes are there:
(a) Abstract classes : Objects CAN’T be instantiated
(b) Concrete classes : Object CAN be instantiated
13) It is mandatory to implement all the pure virtual function in derived class,
otherwise the derived class itself become an Abstract class
14) Pointers of base class can hold the reference to the object of base class
(A very important concept, which is extremely used while write Geant4 simulation code)
Base *ptr = new Derived; // base class holding object of derived class
Derived *derivedPtr = static_cast<Derived*>(basePtr) //casting the base class pointer to derived class

## Slide 5
Geometry in Geant4 (Things to be discussed)
1) Steps involved to create the detector geometries
2) Some of the complex geometries available in Geant4
3) Discussion of “Materials” in brief.
4) Geometry hierarchy in a detector setup.
5) How to import / export the geometry
6) Use of GDML

## Slide 6
Software architecture of Detector geometry
Basically consist of three layers
1) Solid (Shape) : G4VSolid : Defines the shape and size of the geometry
2) Logical Volume : G4LogicalVolume : material, sensitivity, visualization
attributes, physical placement of daughter volumes etc.
3) Physically place volume : G4VPhysicalVolume : defines position, rotatation,
and mother volume

## Slide 7
Various Shapes available in Geant4
Computing volumes and weights
• Geometrical volume of a generic solid or boolean composition can be
computed from the solid volume:
G4double GetCubicVolume();
– Exact volume is determinatively calculated for most of CSG solids, while
estimation based on Monte Carlo integration is given for other solids.
• Overall weight of a geometry setup (sub-geometry) can be computed from the
logical volume:
G4double GetMass(G4bool forced=false,
G4bool propagate=true, G4Material* pMaterial=0);
– The computation may require a considerable amount of time, depending
on the complexity of the geometry.
– The return value is cached and reused until forced=true.
– Daughter volumes will be neglected if propagate=false

## Slide 8
Concept of Half lengths
Geant4 geometry works on the concept of half lengths
Suppose we want to create the box of
[10 cm X 20 cm X 30 cm ] : Required dimension
[5 cm X 10 cm X 15 cm ] : Specified Half length
Same concept is applicable to all the geometries
Cone, Tube, etc.
0,0
5,0
-5,0
-10,0
10,0

## Slide 9
Cone and Polycone
Worth discussing as they are used in frequently in experiment setup.
Cone is same as tube but having different lower and upper radius.
Polycone is something like connecting various cones and tubes one after the another.
double z[8] = {-10., 0., 5., 8., 12., 15., 19, 21};
double rmin[8] = {5., 2., 2., 8., 9, 9, 12., 6};
double rmax[8] = {7., 5., 5., 10., 10, 12, 15, 8};
G4Polycone("LeadBlock",0., 2*M_PI, 8, z, rmin, rmax);
Different constructors exist
G4Polycone("MyPolycone", sPhi, dPhi, numZ, z, rmin, rmax);

## Slide 10
Polycone
double z[8] = {-10., 0., 5., 8., 12., 15., 19, 21};
double rmin[8] = {5., 2., 2., 8., 9, 9, 12., 6};
double rmax[8] = {7., 5., 5., 10., 10, 12, 15, 8};
G4Polycone("LeadBlock",0., 2*M_PI, 8, z, rmin, rmax);

## Slide 11
Boolean Operation
G4SubtractionSolid :
Subtraction of one shape from another.
G4SubtractionSolid( const G4String&pName,
G4VSolid* pSolidA ,
G4VSolid* pSolidB ) ;
G4Box boxA("boxA",3*m,3*m,3*m);
G4Orb orb("orbB",4*m);
G4SubtractionSolid subtracted("subtracted_boxes",&boxA,&orb);
G4UnionSolid:
Union of two shapes.
G4UnionSolid( const G4String&pName,
G4VSolid* pSolidA ,
G4VSolid* pSolidB ) ;
G4UnionSolid union("subtracted_boxes",&boxA,&orb);

## Slide 12
Defining Materials
Material can be define in two ways :
1) Using the exising NIST database provided by Geant4
-- Contains a lot of material as elements, isotopes and compound.
-- Need an object of NistManger class
-- G4NistManager *nist = G4NistManager::Instance();
-- G4Material *world_mat = nist->FindOrBuildMaterial("G4_AIR");
(G4_Pb, G4_Al, G4_Mg, G4_Na .. etc.)
(G4_BAKELLITE, G4_ANTHRACENE etc..)
2) Making your own material that can be defined using the various
classes available
-- Isotope : G4Isotope
-- Element : G4Element
-- Molecules : G4Material
-- Compound and Mixture : G4Material

## Slide 13
Defining Materials
Creating Elements
Finally creating material from elements
Getting Water from NISTManager object
G4Material *world_mat =
nist->FindOrBuildMaterial("G4_WATER");

## Slide 14
Creating Logical Volume and it Physical placement
G4LogicalVolume(G4VSolid* pSolid,
G4Material* pMaterial,
const G4String& name);
G4Box box(“test”, 5*cm, 5*cm, 5*cm);
G4Material Al;
G4LogicalVolume *logicalBox = new G4LogicalVolume(box, Al, “LogicalBox”);
G4PVPlacement(G4RotationMatrix *pRot,
const G4ThreeVector &tlate,
G4LogicalVolume *pLogical,
const G4String& pName,
G4LogicalVolume *pMotherLogical,
G4bool pMany,
G4int pCopyNo,
G4bool pSurfChk=false);
new G4PVPlacement(0,
G4ThreeVector(),
logicalBox,
“PhysicalVolume”,
motherLogicalVol,
false,
0,
true);

## Slide 15
Understanding the Geometry Hierarchy
Raw shapes never forms the part of geometry hierarchy.
Physical placement is alway done for a logical volume.
The geometry hierarchy consist of Mother-Daughter relationship.
One Logical volume contains other Physical Volume daughter volumes
The mother logical volume forms the local coordinate system for all its daughter volumes.
If a mother volume is placed more than once, all its daughter volumes will be there in all physical volumes
Only Exception : World Volume
Its a unique physical volume which contains all the other volume of your detector setup
World volume also forms the global coordinate system.

## Slide 16
Both Box and Orb are placed with respect to world reference frame
Understanding Physical placement in the Geometry Hierarchy
Box is placed with respect to world reference frame
Orb is place with respect to box reference frame

## Slide 17
Both Box and Orb are placed with respect to world reference frame

## Slide 18
Box is placed with respect to world reference frame
Orb is place with respect to box reference frame

## Slide 19
Geometry Hierarchy Tree
World
Box_1
Box_2
Orb
Orb
Complete hierarchy contains 5 shapes
But you had created only 3 shapes.
World, Box and Orb
Mother box contains Orb daughter
Multiple placement of mother box contains all the daugter volumes
Make sure you give proper copy number and name to physical placement

## Slide 20
If the same geometry setup needs to be used in multiple simulations or needs to be used by different people
Geant supported geometry export format
GDML (Graphics Description Markup language)
A portable format, similar to XML.
Can be read by standalone application
Various XML reading libraries are present.
Xerces-C is used by Geant4
Exporting Geometry

## Slide 21
Till now, whatever we understood
    Defining shapes, logical volume and their physical placement
    Define material and attaching them to the shapes to convert them to logical volumes
{
C++
Alternative way to achieve the same thing.
Instead of doing a the detector construction at compile that (as done above),
Idea is to generate it at run time.
Reading a text file (XML)
Benefits : Allows to quickly recreate the full detector construction with very few lines of code
Moving ahead

## Slide 22
XML formatted text file.
It implements hierarcy of volumes in a detector setup as the tree of geometries.
Allows to define the material, and place the volumes.
Makes the detector construction portable, and independent of the remaining simulation code.
GDML : Graphics Description Markup Language

## Slide 23
Language independent
Containing user defined tags.
Can be processed by any library that can process XML.
Provides hierarchal structure, and mother daughter relationship can be easily maintained.
Hierarchical structure make its suitable for object oriented programming.
Benefits of using GDML

## Slide 24
The flow of a default GDML file follows:
1) Definitions
2) Materials
3) Solids
4) Structures
5) Setup
NOTE : Your internet browser is a very useful tool to have a look at the XML file.
Overview of GDML : Various Components

## Slide 25
GDML supports all the solids provided by Geant4
Box
Orb
Sphere
Cone
Tube
Parboloid
Ellipsoid
Polyhedro
Polycone
Torus
Trapezoid
Cut Tube
Segment of a Tube
Twisted tube
Extruded Solids
Tesellated Solids
Tetrahedrons
Twisted Generic Trapezoid
Twisted Box
Various GDML Solids

## Slide 26
All the pieces of GDML

## Slide 27
All the pieces of GDML
<solids> tag of GDML

## Slide 28
<materials> tag of GDML

## Slide 29
Structure tag actually defines how different components of detector setup are arranged.
(Actually shows the mother-daughter relatioship)
Both logical and physical volumes are defined in one structure
It show the hierarchy of detector components.
It consist of sequence of volumes tags, that define your logical volumes.
Each volume tag, keeps a pointer to the associated solid and the material.
Structure actually correponds to the your physical detector
<structure> tag of GDML

## Slide 30
Structures cont...

## Slide 31
Setup contains the pointer to you world volume.
While creating a detector setup using gdml as an input file, we need to return a pointer to world volume from the “Construct” function of DetectorConstruction file.
It is possible to define multiple geometry setup, and chosing different volumes as world volume.
Moreover, we can actually split this geometry description in multiple file, which allows more granularity, and ease of maintainance.
Finally the <setup> tab

## Slide 32
The GDML files can be imported directly into Geant4, in the detector construction class
Required class : G4GDMLParser : (#include <G4GDMLParser.hh>)
As usual this class contains various functions :
We will focus on Write and Read
An object of “G4GDMLParser” class is required.
G4GDMLParser myGDMLParser;
To export a full detector construction written in C++
myGDMLParser.Write(“geom.gdml”,pointerToPhyWorld);
To import a full detector setup, just do
myGDMLParser.Read(“geom.gdml);
Finally return the pointer to physical world volume to Geant.
return MyGDMLParser.GetWorldVolume()
NOTE : Geant4 needs to be compile with xercesC library
Exporting/ Importing GDML into Geant4

## Slide 34
Building Complete GEANT application
-- Basic Structure of Geant4 Code
-- Where to write what

## Slide 35
Geant4 Analogy of real experiment
Basic structure of the simulation code.
Writing a basic simulation code
Mandatory classes for your simulation code.
-- Implementation of these mandatory classes
Getting the required information out of you simulation
-- Optional classes
-- Implementation of these optional classes
Things to be discussed

## Slide 36
Geant4 Analogy of the real experiment setup
Beam On : As in real experiment the Geant4 run starts with “Beam On”
A run is basically a collection of event.
As in experiment once the run start, user cannot change anything
--> Geometry Setup
--> Physics processes to study
Before starting the run, following things need to be initialized
--> Detector setup (geometry is optimized)
--> Physics List (cross-section tables are calculated, depending upon the materials used in the geometry creation)

## Slide 37
Important user classes : Geant4 Program structure
Define your entry point : main() : There is no starting point provided by Geant4.
It is the place where you actually registers different component of you application.
Initialization classes : Classes whose objects needs to initiated before you simulation starts.
Detector : G4VUserDetectorConstruction
Physics : G4VUserPhysicsList / Existing or Implemented
UserActions : G4VUserActionInitialization
Action classes :
instantiated in the G4VUserActionInitialization
The action classes are invoked during the event loop : ie. When you simulation is running.
The classes starting with G4V are abstract classes.
Their objects can’t be created.
They are there to provide a skeleton required by Geant4
User needs to inherit these classes, and to implement few functions which are mandatory.
G4VUserPrimaryGeneratorAction
G4UserRunAction
G4UserEventAction
G4UserStackingAction
G4UserTrackingAction
G4UserSteppingAction

## Slide 38
Creation of your DetectorConstruction : G4VUserDetectorConstruction
class G4VUserDetectorConstruction
{
public:
G4VUserDetectorConstruction();
virtual ~G4VUserDetectorConstruction();
virtual G4VPhysicalVolume* Construct() = 0;
};
class Sim01_DetectorConstruction : public G4VUserDetectorConstruction
{
public:
Sim01_DetectorConstruction(){}
~Sim01_DetectorConstruction(){}
G4VPhysicalVolume* Construct(){
//Write your stuff here
//construct all your materials
//construct all your volumes
//declare you volume as sensitive
}
};
(Pure virtual function)
The Construct method should return the pointer to the world physical volume, which represents your entire geometry setup.

## Slide 39
There is no default particles and physics process that comes automatically in your simulation code.
Not even particle transport.
Derive your own concrete class from G4VUserPhysicsList abstract base class.
– Define all necessary particles
– Define all necessary processes and assign them to proper particles
– Define all the required cut-off ranges
OR use the various physics lists that are already available in GEANT4.
FPFP_BERT (add few more list)
Define your Physics

## Slide 40
Primary Generator : G4VUserPrimaryGeneratorAction
The second mandatory user class : Controls the generation of primary particles.
--> This is again a abstract class
--> You cannot instantiate it : Will not do anything on its own
class G4VUserPrimaryGeneratorAction
{
G4VUserPrimaryGeneratorAction();
virtual ~G4VUserPrimaryGeneratorAction();
virtual void GeneratePrimaries(G4Event* anEvent) = 0;
};
class Sim01_PrimaryGeneratorAction : public G4VUserPrimaryGeneratorAction
{
G4ParticleGun *fParticleGun;
Sim01_PrimaryGeneratorAction(){}
~Sim01_PrimaryGeneratorAction(){}
void GeneratePrimaries(G4Event*){
fParticleGun->GeneratePrimaryVertex();
}
};
The generate primaries method is called at the beginning of every event.
Your primary generator will not generate any primary particle, until you call GeneratePrimaryVertex() function

## Slide 41
Sim01_PrimaryGeneratorAction::Sim01_PrimaryGeneratorAction() {
int numOfParticle = 1;
fParticleGun = new G4ParticleGun(numOfParticle);
G4ParticleTable *particleTable = G4ParticleTable::GetParticleTable();
G4ParticleDefinition *particle = particleTable->FindParticle("mu-");
fParticleGun->SetParticleDefinition(particle);
fParticleGun->SetParticleMomentumDirection(G4ThreeVector(0.,0.,-1.));
fParticleGun->SetParticleEnergy(3.*GeV);
fParticleGun->SetParticlePosition(G4ThreeVector(0.,0.,30.*cm));
}
void Sim01_PrimaryGeneratorAction::GeneratePrimaries(G4Event *event) {
fParticleGun->SetParticleMomentumDirection(G4RandomDirection());
fParticleGun->GeneratePrimaryVertex(event);
}
Called only once
Called in the beginning of every event

## Slide 42
Run Manager : G4RunManager
One of the manager class in Geant4 .
Helps in linking various objects and modules required during the initialization and run.
The program cannot run without the Run Manager.
User can inherit in their derived class to customize the behaviour
G4RunManager or its Derived class must be singleton
--> Only one object should exist in the program’s memory.
Singleton instance helps in accessing the same RunManager object in different locations in the code.

## Slide 43
Action Initialization : G4VUserActionInitialization
Basically used to instantiate various classes required during event loop
class Sim01_ActionInitialization : public G4VUserActionInitialization
{
public:
Sim01_ActionInitialization(){}
virtual ~Sim01_ActionInitialization(){}
virtual void BuildForMaster() const{}
virtual void Build() const{
// Link the objects of classes invoked
during the event loop
// EventAction, SteppingAction
}
};
class G4VUserActionInitialization
{
G4VUserActionInitialization();
virtual ~G4VUserActionInitialization();
virtual void Build() const = 0;
}

## Slide 44
Define your entry point : main() :The place where you actually registers different components of your application.
Things TODO:
1) Instantiate your RunManager
2) Instantiate your DetectorConstruction
3) Instantiate your PhysicsList
4) Instantiate your ActionInitialization
5) Run your code
Optional
6) Instantiate your Visualization Manager
Structure of main() function
Int main(){
G4RunManager *runManager = new G4RunManager;
DetectorConstruction *det = new DetectorConstruction();
G4VModularPhysicsList *physicsList = new FTFP_BERT;
ActionInitialization *actIni = new ActionInitialization();
runManager->SetUserInitialization(det);
runManager->SetUserInitialization(physicsList);
runManager->SetUserInitialization(actIni);
G4UImanager *UImanager = G4UImanager::GetUIpointer();
Uimanager->ApplyCommand(“/control/execute Run.mac”);
}
/run/initialize
/run/beamOn 100
Run.mac

## Slide 45
Our program is running : Where is the output ??
Geant4 runs the full simulation silently.
The required information needs to extracted.
Just to see what going on :
--> use UI commands : /tracking/verbose 1
This will basically start printing all the tracking information.
--> Particle information (location, direction etc.)
--> Step information
--> Energy loss
--> Associated volume
--> TrackId

## Slide 47
Geant4 Classes to get the information from the simulations
Information can be fetched at different levels, depending upon the requirements.
--> Run level information (G4UserRunAction)
--> Event level information (G4UserEventAction)
--> Step level information (G4UserSteppingAction)
--> Few more are also there.
These will be discussed in detail in the coming talks.

## Slide 48
Thanks for your attention