## Slide 1: Geant4 Physics List for NaI(Tl) Detector
Simulating Gamma-Ray Interactions and Radioactive Decay

## Slide 2: Why Do We Need a Physics List for NaI Simulations?
- Geant4 does not include physics by default.
- Physics List determines how particles interact with materials.
- Different interactions are crucial for NaI(Tl) response.

## Slide 3: Key Physics in NaI(Tl) Simulations
✔ Gamma interactions: Photoelectric effect, Compton scattering, Pair production
✔ Radioactive decay: Simulates isotopes like Cs-137
✔ Scintillation: Converts gamma energy into optical photons
✔ Optical physics: Tracks scintillation light to the PMT

## Slide 4: Choosing the Right Physics List
✅ Electromagnetic physics (G4EmStandardPhysics) - Handles gamma-ray interactions
✅ Decay physics (G4DecayPhysics) - Handles generic particle decays
✅ Radioactive decay (G4RadioactiveDecayPhysics) - Simulates source decay
✅ Optical physics (G4OpticalPhysics) - Tracks scintillation light

## Slide 5: Breakdown of Physics Components
1. G4EmStandardPhysics (Electromagnetic Interactions)
- Photoelectric Effect: Dominates at low energy (<100 keV)
- Compton Scattering: Main interaction for 662 keV gamma rays
- Pair Production: Only occurs for E > 1.022 MeV
2. G4RadioactiveDecayPhysics (Simulating Sources)
- Example: Cs-137 → Ba-137m + β⁻
- Ensures realistic emission spectrum
3. G4OpticalPhysics (Scintillation & Optical Photons)
- Converts gamma energy into visible light
- Tracks light propagation to PMT

## Slide 6: Implementing the Physics List
```cpp
RegisterPhysics(new G4EmStandardPhysics()); // Gamma interactions
RegisterPhysics(new G4DecayPhysics()); // Generic particle decays
RegisterPhysics(new G4RadioactiveDecayPhysics()); // Cs-137, Co-60 decays
RegisterPhysics(new G4OpticalPhysics()); // Scintillation and light transport
```
📌 Takeaway: This setup ensures accurate NaI(Tl) response simulation!

## Slide 7: Impact of Choosing the Right Physics
❌ Without G4RadioactiveDecayPhysics:
- No Cs-137 decay → No 662 keV gamma emission
- No realistic energy spectrum
❌ Without G4OpticalPhysics:
- No scintillation → PMT gets no light
✅ With full Physics List:
- Accurate gamma detection
- Realistic energy spectrum

## Slide 8: Summary & Key Takeaways
✔ Physics List is critical for realistic NaI(Tl) simulations
✔ G4EmStandardPhysics: Handles gamma interactions
✔ G4RadioactiveDecayPhysics: Simulates radioactive sources
✔ G4OpticalPhysics: Tracks scintillation light
📢 A well-configured Physics List ensures accurate detector response!

## Slide 9: Q&A and Discussion
- Invite questions on specific physics models
- Discuss real-world applications (e.g., medical imaging, radiation monitoring)